## Slide 2: Computer Organization & Design
The Hardware/Software Interface

## Slide 3: Chapter 2 Instructions: Language of the Machine
3

## Slide 4: Contents of Chapter 2
4
2.1 Introduction
2.2 Operations of the Computer Hardware
2.3 Operands of the Computer Hardware
2.4 Instruction format
2.5 Instructions for Making Decisions
2.6 Supporting Procedures in Computer Hardware
2.7 Beyond Numbers

## Slide 5
5
2.8 Starting a Program
2.9 An Example To Put it All Together
2.10 Arrays versus Pointers
2.11 PowerPC and 80x86 Instructions
2.12 History of Instruction Set Development
2.13 Summary

## Slide 6: 2.1 Introduction
6
Language of the machine
  Instructions
  Instruction set
Design goals
  Maximize performance
  Minimize cost
  Reduce design time
Our chosen instruction set: MIPS

## Slide 7: 2.2 Operations of the Computer Hardware
7
Every computer must be able to perform arithmetic:
  add a, b, c # a=b+c
  Exactly three variables
Design Principle 1
  Simplicity favors regularity

## Slide 8: Example 2.1
8
Compiling two simple C statements
  C code:
  a = b + c;
  d = a – e;
  MIPS code:
  add a, b, c
  sub d, a, e

## Slide 9
  Example 2.2 Compiling a complex C statement
  C code:
  f = ( g + h ) – ( i + j );
  MIPS code:
  add t0, g, h # temporary variable t0 contains g + h
  add t1, i, j # temporary variable t1 contains i – j
  sub f, t0, t1 # f gets t0 – t1

## Slide 10: 2.3 Operands of the Computer Hardware
10
Arithmetic instruction’s operands must be in registers
  32 registers in MIPS
  32 bits for each register in MIPS
Design Principle 2
  Smaller is faster
MIPS convention for registers
  $s0, $s1, … for registers corresponding to variables in C
    register int i;
  $t0, $t1, … for temporary registers

## Slide 11
11
Example 2.3 Compiling a C statement using registers
  C code
  f = ( g + h ) – ( i + j ) ;
  MIPS code
  add $t0, $s1, $s2 # $t0 contains g + h
  add $t1, $s3, $s4 # $t1 contains i + j
  sub $s0, $t0, $t1 # f ($S0)gets $t0 - $t1
Data transfer instructions
  Memory address
  Load: from memory to register; load word ( lw )
  Store: from register to memory; store word ( sw )
谁在做LW，SW？
  编译器，操作系统

## Slide 12: Memory addresses and contents at those locations
12

## Slide 13
13
Example 2.4 Compiling with an operand in memory
( Assume: g ---- $s1 h ---- $s2 base address of A ---- $s3 )
  C code:
  g = h + A[8] ; // A is an array of 100 words
  MIPS code:
  lw $t0, 8($s3) # temporary reg $t0 gets A[8]
  add $s1, $s2, $t0 # g = h + A[8]
  Offset: the constant in a data transfer instruction
  Base register: the register added to form the address
Byte addressing
Alignment restriction
  Addresses of words are multiples of 4 in MIPS

## Slide 14: Actual MIPS memory addresses and contents
14

## Slide 15: Memory Alignment
15
struct {
int a;
char b;
char c[2];
char d[3]
float e;
}
a
b
e
No use
No use
No use
C[0]
C[1]
No use
No use
D[0]
d[1]
D[2]
No use
D[0]
d[1]
D[2]
e
e
No use
错误
因为内存一次只能读出4字节内存中的一行
这样布局，e变量不能一次读出

## Slide 16
16
Example 2.5 Compiling using load and store
  ( Assume: h ---- $s2 base address of A ---- $s3 )
  C code:
  A[12] = h + A[8] ; // A is an array of 100 words
  MIPS code:
  lw $t0 , 32($s3) # temporary reg $t0 gets A[8]
  add $t0, $s2, $t0 # temporary reg $t0 gets h + A[8]
  sw $t0, 48($s3) # stores h + A[8] back into A[12]

## Slide 17
17
Example 2.6 Compiling using a variable array index
  ( Assume: g, h, i ---- $s1, $s2, $s4 base address of A ---- $s3 )
  C code:
  g = h + A[i] ; // A is an array of 100 words
  MIPS code:
  add $t1, $s4, $s4 # temp reg $t1 = 2 * i
  add $t1, $t1, $t1 # temp reg $t1 = 4 * i
  add $t1, $t1, $s3 # $t1 = address of A[i] (4 * i + $s3)
  lw $t0 , 0($t1) # temp reg $t0 = A[i]
  add $s1, $s2, $t0 # g = h + A[i]
Spilling registers

## Slide 18
18
int i;
int A[3];
int j;
FFFF FFFF
0000 0000
i
A
j
PUSH
POP
STACK

## Slide 19
19
int i,A[3], j;
…
j=A[3];
The result j=?
A
A[0]
A[1]
A[2]
A[3]

## Slide 20: 2.4 Instruction Format
20
All information in computer consists of binary bits
Mapping registers into numbers
  Map registers $s0 to $s7 onto registers 16 to 23
  Map registers $t0 to $t7 onto registers 8 to 15
Example 2.7 Translating assembly into machine instruction
  MIPS code
  add $t0, $s1, $s2
  Decimal version of machine code
  | 0 | 17 | 18 | 8 | 0 | 32 |
  Binary version of machine code
  | 000000 | 10001 | 10010 | 01000 | 00000 | 100000 |
  6 bits 5 bits 5 bits 5 bits 5 bits 6 bits

## Slide 21
21
MIPS fields
  R-type or R-format
| op | rs | rt | rd | shamt | funct |
  6 bits 5 bits 5 bits 5 bits 5 bits 6 bits
  I-type or I-format
| op | rs | rt | address |
  6 bits 5 bits 5 bits 16 bits
  Op: Basic operation of the instration opcode
  Rs: The first register source operand.
  Rt: The second register source operand.
  Rd: The register destination operand.
  Shamt: Shift amount.
  Funct: Function.

## Slide 22
22
Design Principle 3
  Good design demands good compromises
All instructions in MIPS have the same length(32 bits)

## Slide 23
23
Example 2.8 Translating assembly into machine instruction
( Assume: h ---- $s2 base address of A ---- $t1 )
  C code:
  A[300] = h + A[300] ;
  MIPS assembly code:
  lw $t0, 1200($t1) # temporary reg $t0 gets A[300]
  add $t0, $s2, $t0 # temporary reg $t0 gets h + A[300]
  sw $t0, 1200($t1) # stores h + A[300] back into A[300]
  MIPS machine language code:
    Decimal version address/
    op rs rt rd shamt funct
  | 35 | 9 | 8 | 1200 |
  | 0 | 18 | 8 | 8 | 0 | 32 |
  | 43 | 9 | 8 | 1200 |

## Slide 24
24
    Binary version
  | 100011 | 01001 | 01000 | 0000 0100 1011 0000 |
  | 000000 | 10010 | 01000 | 01000 | 00000 | 100000 |
  | 101011 | 01001 | 01000 | 0000 0100 1011 0000 |
  Note the only difference of the first and last instructions!
Two key principles of today’s computers
  Instructions are represented as numbers
  Programs can be stored in memory to be read or
  written just like number
  The principles are the stored program concept

## Slide 25
25
    Two key principles of today’s computers
  Instructions are represented as numbers
  Programs can be stored in memory to be read or
  written just like numbers

## Slide 26
26
Stored-program concept

## Slide 27: 任务管理器1
27
Ctrl+alt+del
  只能被MS截获
列出所有正在运行的任务
  任务的内存大小
  任务的CPU占有率
  任务的CPU时间
  PID为进程号
    越大越晚启动

## Slide 28
28
重新启动explorer
  可以杀explorer进程
  在应用程序中运行新任务,输入explorer即可

## Slide 29: Trojan 最简单例子-密码窃取
main() {
char password[256], crypt_pw[256];
scanf(“%s”,password);
crypt(password, crypt_pw);
if ( strcmp(crypt_pw, “xxxxxx”)!=0 )
printf(“password error\n”);
else
;
}
Input: 123456
Trojan read memory variable “password”
123456
abcdef
a.exe
trojan
password
Crypt_pw

## Slide 30: 变形病毒原理
30
000000 | 10010 | 01000 | 01000 | 00000 | 100000
op rs rt rd shamt funct
ADD t0, s2, t0
00000010010010000100000000100000
Memory addr: 0x40000008
main() {
int *p;
p=0x40000008;
*p+=2
}
000000 | 10010 | 01000 | 01000 | 00000 | 100010
SUB t0, s2, t0
问题：如果这是一个执行程序拳击游戏，该行指令表示您挨打，血(t0)在减少(s2为负数)，当血小于等于0，KO。
用ultraedit将该二进制执行文件修改，让自己不损血，怎么改？

## Slide 31: Demo:Edit the execute file and memory
31
Change the program info(static)
  Use hex edit tools
  Eg:use ultraedit, change title
    Leapftp -> leepftp
Change the program info(run time)
  Use memory edit tools
  Eg:use 金山游侠, change data

## Slide 32: 脱壳shell
32
一个执行程序，有判断是否为盗版，问如何crack
查找判断之处，找到后看变量作用位置
找到惩罚处，将该处的二进制代码改成noop
main() {
int expired=false;
calculate expired；
if (expired) {
printf(“软件过期了\n”);
exit(1); -> “;” -> noop
}
else ..
}

## Slide 33: 变量初始值例子
33
1.C
main(){
int k=65;
}
Compile and run it
Modify 1.c
main(){
char m;
printf(“%c\n”,m);
}
Compile and run it
0x 00 00 00 41
k
0x 00 00 00 0a
m
m=0x41=‘a’
条件：无其他程序在运行

## Slide 34: 2.5 Instructions for making decisions
34
Branch instructions (条件转移指令)
  beq register1, register2, L1 # R1-R2=0 GOTO L1
  bne register1, register2, L1 #R1-R2 NE 0 GOTO L1
Example 2.9 Compiling an if statement to a branch
( Assume: f ~ j ---- $s0 ~ $s4 )
  C code:
  if ( i = = j ) goto L1 ;
  f = g + h ;
  L1: f = f - i ;
  MIPS assembly code:
  beq $s3, $s4, L1 # go to L1 if i equals j
  add $s0, $s1, $s2 # f = g + h ( skipped if i equals j )
  L1: sub $s0, $s0, $s3 # f = f - i ( always executed )

## Slide 35
35
Example 3.10 Compiling an if-then-else statement
( Assume: f ~ j ---- $s0 ~ $s4 )
  C code:
  if ( i = = j ) f = g + h ; else f = g - h ;
  MIPS assembly code:
  bne $s3, $s4, Else # go to Else if i != j
  add $s0, $s1, $s2 # f = g + h ( skipped if i != j )
  j Exit # go to Exit
  Else: sub $s0, $s1, $s2 # f = g - h ( always executed )
  Exit:
  Note: J Exit instruction function is : no condition Address Exit move to PC
  . Assume: Exit=1000 then PC=1000

## Slide 36: The options in the if statement above
36
Flow Chart:

## Slide 37
37
Example 2.11 Compiling a loop with variable array index
( Assume: g ~ j ---- $s1 ~ $s4 base of A ---- $s5)
  C code:
  Loop: g = g + A[i] ; // A is an array of 100 words
  i = i + j ;
  if ( i != h ) goto Loop ;
  MIPS assembly code:
  Loop: add $t1, $s3, $s3 # temp reg $t1 = 2 * i
  add $t1, $t1, $t1 # temp reg $t1 = 4 * i
  add $t1, $t1, $s5 # $t1 = address of A[i]
  lw $t0, 0($t1) # temp reg $t0 = A[i]
  add $s1, $s2, $t0 # g = g + A[i]
  add $s3, $s3, $s4 # i = i + j
  bne $s3, $s2, Loop # go to Loop if i != h

## Slide 38
38
Example 2.12 Compiling a while loop
( Assume: i ~ k---- $s3 ~ $s5 base of save ---- $s6 )
  C code:(当语句)
  while ( save[i] = = k )
  i = i + j ;
  MIPS assembly code:
  Loop: add $t1, $s3, $s3 # temp reg $t1 = 2 * i
  add $t1, $t1, $t1 # temp reg $t1 = 4 * i
  add $t1, $t1, $s6 # $t1 = address of save[i]
  lw $t0, 0($t1) # temp reg $t0 = save[i]
  bne $t0, $s5, Exit # go to Exit if save[i] != k
  add $s3, $s3, $s4 # i = i + j
  j Loop # go to Loop
  Exit:

## Slide 39
39
Example 2.13 Compiling a less than test
( Assume: a ---- $s0 b ---- $s1 )
  Condition: if variable a is less than b, branch to label Less
  MIPS assembly code:
  slt $t0, $s0, $s1 # $t0 gets 1 if $s0 < $s1 ( a < b)
  # $s0-$s1<0 ,test sign bit =1
  bne $t0, $zero, Less # go to Less if $t0 != 0 (that is, if
  #a < b )
  $Zero: 0 constant; $1: reserved for compile

## Slide 40
40
Example 2.14 Compiling a switch using jump address table
( Assume: f ~ k ---- $s0 ~ $s5 $t2 contains 4 )
C code:
switch k { case 0 : f = i + j ; break ; /* k = 0 */
  case 1 : f = g + h ; break ; /* k = 1 */
  case 2 : f = g - h ; break ; /* k = 2 */
  case 3 : f = i - j ; break ; /* k = 3 */
  }

## Slide 41: Jump register & jump address table
41
Jump with register content
jr $r
jump address table
K=0 | P1 address
K=1 | P2 address
K=2 | P3 address
K=3 | P4 address
$t4
 | …………
P1 address | Program 1
 | …………
P2 address | Program 2
 | …………
P3 address | Program 3
 | …………
P4 address | Program 4
 | …………
$r←$t4+4*K

## Slide 42
  MIPS assembly code:
  slt $t3, $s5, $zero # test if k < 0
  bne $t3, $zero, Exit # if k < 0, go to Exit
  slt $t3, $s5, $t2 # test if k < 4
  beq $t3, $zero, Exit # if k >=4, go to Exit
  add $t1, $s5, $s5 # temp reg $t1 = 2 * k
  add $t1, $t1, $t1 # temp reg $t1 = 4 * k
  add $t1, $t1, $t4 # $t1 = address of JumpTable[k]
  lw $t0, 0($t1) # temp reg $t0 = JumpTable[k]
  jr $t0 # jump based on register $t0
  L0: add $s0, $s3, $s4 # k = 0 so f gets i + j
  j Exit # end of this case so go to Exit
  L1: add $s0, $s1, $s2 # k = 1 so f gets g + h
  j Exit # end of this case so go to Exit
L2: sub $s0, $s1, $s2 # k = 2 so f gets g - h
  j Exit # end of this case so go to Exit
  L3: sub $s0, $s3, $s4 # k = 3 so f gets i - j
  Exit: # end of switch statement

## Slide 43
43
  Tech. Need design an address jumptable[]
L0=1000
L1=2000
L3=4000
L2=3000
K=0
K=1
K=2
K=3
表头地址

## Slide 44: 2.6 Supporting Procedures in Computer Hardware
44
Six steps for execution of the procedure
  1.Main program to place parameters in place where the procedure can access them
  2. Transfer control to the procedure
  3. Acquire the storage resources needed for the procedure (保护过程要用的寄存器)
4.Perform the desired task
5. Return result value to main program
6. Return control to the point of origin(即断点)

## Slide 45
45
Registers for procedure calling
  $a0 ~ $a3: four argument registers to pass parameters
  $v0 ~ $v1: two value registers to return values
  $ra: one return address register to return to origin point
Instruction for procedures: jal ( jump-and-link )
jal ProcedureAddress
Its main function
1). Next instruction address (PC+4 )Save to $ra ($31)
2). Procedure Address move to PC(instruction address REG.)
return control to the caller using Jr $ra ($31)
Using more registers
  Stack: ideal data structure for spilling registers
  Stack Operation :Push, pop ; Stack pointer: $sp ($29)

## Slide 46
46
MIPS STACKS Grow from higher address to lower address:
Push : sp=sp-4
Pop:sp=sp+4
SP=SP-4
SP=SP+4
STACK

## Slide 47
47
Example 2.11 Compiling a leaf procedure
( Assume: g ~ j ---- r0 ~ r3 f ---- r4 for the rest of this section we assume we can add or subtract constants )
  C code:
  int leaf_example ( int g, int h, int i, int j )
  {
  int f ;
  f = ( g + h ) - ( i + j ) ;
  return f ;
  }

## Slide 48
48
  MIPS assembly code:
  Leaf: addi $sp, $sp, -12 # adjust stack to make room for 3 items
  sw $t1, 8($sp) # save register $t1 for use afterwards
  sw $t0, 4($sp) # save register $t0 for use afterwards
  sw $s0, 0($sp) # save register $s0 for use afterwards
add $t0, $a0, $a1 # register $t0 contains g + h
add $t1, $a2, $a3 # register $t1 contains i + j
sub $s0, $t0, $t1 # f= $t0 -$t1, which is ( g+h ) – ( i+ j )
add $v0, $s0, $zero # returns f ( $v0 = $s0 + 0)
lw $s0, 0($sp) # restore register $s0 for caller
lw $t0, 4($sp) # restore register $t0 for caller
lw $t1, 8($sp) # restore register $t1 for caller
add $sp, $sp, 12 # adjust stack to delete 3 items
jr $ra # jump back to calling routine

## Slide 49
49
Caller: 主调程序 ; CALLEE –Called procedure 被调程序
Two classes of registers
  $t0 ~ $t9: 10 temporary registers , not preserved
  $s0 ~ $s7: 8 saved registers, must be preserved

## Slide 50: The values of the stack pointer and stack before, during and after procedure called
50

## Slide 51
51
Nested Procedures
Example 2.16 Compiling a recursive procedure
( Assume: n ---- $a0 )
  C code
  int fact ( int n )
  {
  if ( n < 1 ) return ( 1 ) ;
  else return ( n * fact ( n - 1 ) ) ;
  }
  Assume MAIN program: jal fact # n=2
  断点返回1000
  设主程序:
  996: Jal fact
  1000: add $s1, $s2, $s3

## Slide 52
52
  MIPS assembly code fact:
  Fact: addi $sp,$sp,-8 # adjust stack for 2 items
  sw $ra, 4($sp) # save the return address
  sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # test for n < 1
beq $t0, $zero, L1 # if n >= 1, go to L1
add $v0, $zero, 1 # return 1
add $sp, $sp, 8 # pop 2 items off stack
jr $ra # return to after j
L1: addi $a0, $a0, -1 # n >= 1, n=n-1
jal fact # call fact with ( n - 1 )
2000 : lw $a0, 0($sp) # return form jal: restore argument n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # adjust stack pointer to pop 2 items
mul $v0, $a0, $v0 # return n * fact ( n - 1 )
jr $ra # return to the caller

## Slide 53
53
Assume Main code is:
996: jal fact
1000: add $s1,$s2,$s3
And L1=1992(十进制)
Preserved things across a procedure call
Saved registers( $s0 ~ $s7 ), stack pointer register( $sp ),
return address register( $ra )
Not preserved things across a procedure call
Temporary registers( $t0 ~ $t9 )
主程序传递给子程序的 argument registers( $a0 ~ $a3 )
return value registers( $v0 ~ $v1)

## Slide 54
54
SP
SP-16
1000
2
1
2000
1000
2
1
2000
SP-16
1000
2
SP-8
初始 主程序第一次 第一次递归调用 第二次递归调用 N<1时
CALL FACT FACT FACT
SP-24
1000
2
1
2000
2000
0

## Slide 55: Stack allocation before, during and after procedure call
55

## Slide 56
56
Procedure frame and frame pointer ( $fp )
  $fp offers a stable base register
  Adjust stack only on entry and exit of procedure to avoid $fp
Storage class of C variables
  automatic
  static
Global pointer ( $gp ) 指向静态变量 static variables

## Slide 57: 最经典的黑客技术原理-缓冲区溢出
57
微机中，没有a0-a3，传递参数都是通过堆栈
函数调用将压入堆栈以下数据：ra，sfp，参数。
main() {
…
fun(a);
}
fun(int b){
char c[4];
printf(“%x\n”,c[4]);
c[12]=c[13]=c[14]=c[15]=0x40;
}
ra
Sfp
a
C[4]
微机的汇编：ret，函数返回

## Slide 58: 2.7 Beyond Numbers (character) 字符指令
58
ASCII ( American Standard Code for Information Interchange )
Instructions for moving bytes in MIPS
  Load byte ( lb ): lb $t0, 0($sp) # read byte from source
  Store byte ( sb ): sb $t0, 0($sp) # write byte to destination
Three choices for representing a string(三种方法)
  Place the length of the string in the first position
  An accompanying variable has the length in 结构中
  A character in the last position to mark the end of a string
C uses the third choice
  Terminate a string with a byte whose value is 0 ( null in ASCII )

## Slide 59
59
Example 2.17 Compiling a string copy procedure
( Assume: base addresses for x and y ---- $a0 and $a1 i ---- $s0 )
  C code:
  void strcpy ( char x[ ] , char y[ ] )
  {
  int i ;
  i = 0 ;
  while ( ( x[ i ] = y[ i ] ) != 0 ) /* copy and test byte */
  i = i + 1 ;
  }

## Slide 60
60
  MIPS assembly code:
  strcpy: addi $sp, $sp, -4 # adjust stack
  sw $s0, 0($sp) # save $s0
  add $s0, $zero, $zero # i = 0 + 0
  L1: add $t1, $a1, $s0 # address of y[ i ] in $t1
  lb $t2, 0($t1) # $t2 = y [ i ]
  add $t3, $a0, $s0 # address of x[ i ] in $t3
  sb $t2, 0($t3) # x[ i ] = y[ i ]
add $s0, $s0, 1 # i = i + 1
bne $t2, $zero, L1 # if y[ i ] != 0, go to L1
lw $s0, 0($sp) # y[ i ] = = 0: end of string;
# restore old $s0
add $sp, $sp, 4 # pop 1 word off stack
jr $ra # return

## Slide 61
61
Optimization for example 2.17
  strcpy is a leaf procedure
  Allocate i to a temporary register $t0
For a leaf procedure
  The compiler exhausts all temporary registers
  Then use the registers it must save

## Slide 62: 2.8 Other Styles of MIPS Addressing
62
Immediate addressing(立即数寻址)
  Constant or immediate operands
  I-format instructions
Example 2.18 Translating assembly constants to machine code
  MIPS code:
  addi $sp, $sp, 4 # $sp = $sp + 4
  Machine code:
    Decimal version
    op rs rt immediate
  | 8 | 29 | 29 | 4 |
    Binary version
  | 001000 | 11101 | 11101 | 0000 0000 0000 0100 |

## Slide 63
63
Design Principle 4
  Make the common case fast
Example 2.19 Loading a 32-bit constant
  The 32-bit constant:
  0000 0000 0011 1101 0000 1001 0000 0000
  MIPS code:
  lui $s0, 61 # 61 decimal = 0000 0000 0011 1101 binary
  (The value of $s0 afterward is: 0000 0000 0011 1101 0000 0000 0000 0000)
  addi $s0, $s0, 2304 # 2304 decimal = 0000 1001 0000 0000 binary
  (The value of $s0 afterward is: 0000 0000 0011 1101 0000 1001 0000 0000)
  ori $s0,$s0,2304 ulw $s0,32bits(伪指令)
The reserved register $at for the assembler

## Slide 64
64
Addressing in branches and jumps
  For jumps: J-format
    Example:
  j 10000 # go to location 10000
  | 2 | 10000 |
  6 bits 26 bits
    Pseudodirect addressing
    26 bits of the instruction concatenated with the upper 4 bits of PC
  Note: 10000 is word address
  PC High 4bits.26bitsx4 move to PC Form
  Jump address

## Slide 65
65
  For branches: Example
    bne $s0, $s1, Exit # go to Exit if $s0 != $s1
  | 5 | 16 | 17 | offset |
  6 bits 5 bits 5 bits 16 bits
    PC-relative addressing, Why?
    Program counter = (PC+4) + offset x4
    PC= (PC+4) + offset x4
    Ex:
    100: bne $s0, $s1, Exit #if $s0=$s1 then PC=?
    104: add $t1, $t2, $t3
    if $s0!=$s1 Answer: PC=104+ (offset)x4=104+8x4=136

## Slide 66
66
PC-relative addressing(PC相对寻址)
PC
PC+4
BNE SKIP
低地址
高地址
-32768

## Slide 67
67
Example 2.20 Show branch offset in machine language
  MIPS assembler code in Example 3.12:
  Loop: add $t1, $s3, $s3 # temp reg $t1 = 2 * i
  add $t1, $t1, $t1 # temp reg $t1 = 4 * i
  add $t1, $t1, $s6 # $t1 = address of save[i]
  lw $t0, 0($t1) # temp reg $t0 = save[i]
  bne $t0, $s5, Exit # go to Exit if save[i] != k
  add $s3, $s3, $s4 # i = i + j
  j Loop # go to Loop
  Exit:

## Slide 68
68
  Assembled instructions and their addresses:
80000 | 0 | 19 | 19 | 9 | 0 | 32 |add
80004 | 0 | 9 | 9 | 9 | 0 | 32 |add
80008 | 0 | 9 | 22 | 9 | 0 | 32 |add
80012 | 35 | 9 | 8 | 0 |LW
80016 | 5 | 8 | 21 | 2 |bne
80020 | 0 | 19 | 20 | 19 | 0 | 32 |add
80024 | 2 | 20000 |j loop
80028 . . .
Modification:
    All MIPS instructions are 4 bytes long
    PC-relative addressing refers to the number of words
    80020+2x4=80028>PC

## Slide 69
69
Example 3.21 Branching far away
  Given a branch:
  beq $s0, $s1, L1
  Rewrite it to offer a much greater branching distance:
    bne $s0, $s1, L2
    j L1
    L2:
MIPS addressing mode summary
  1). Register addressing
  2).Base or displacement addressing
  3).Immediate addressing
  4).PC-relative addressing
  5). Pseudodirect addressing

## Slide 70: MIPS addressing modes
70

## Slide 71
71
Example 2.22 Decoding machine code(A23, P153)
  Machine instruction(将机器指令手工翻译成汇编指令)
  ( Bits: 31 28 26 5 2 0 )
  0000 0000 1010 1111 1000 0000 0010 0000
  Decoding
    Determine the operation from opcode
    op: 000000  R-format instruction
    op rs rt rd shamt funct
  | 000000 | 00101 | 01111 | 10000 | 00000 | 100000 |
    funct: 100000  add instruction
    Determine other fields 注:A23为寄存器名--值对照表)
    rs: $a1 rt: $t7 rd: $s0 P153指令操作码对照表
    Show the assembly instruction
    add $s0, $a1, $t7

## Slide 72: **Summary of MIPS architecture in Chapter 2
72
MIPS instruction format
| Name | Fields | Comments |
| Field size | 6 bits| 5 bits| 5 bits| 5 bits| 5 bits| 6 bits| All MIPS instructions 32 bits |
| R-format | op | rs | rt | rd |shamt| funct | Arithmetic instruction format |
| I-format | op | rs | rt | address/immediate | Transfer,branch,imm. format |
| J-format | op | target address | Jump instruction format |
MIPS operands
| Name | Example |
| 32 registers | $s0~$s7, $t0~$t9,$zero, $a0~$a3, $v0~$v1, $fp, $gp, $ra, $at |
| Mem words | Memory[0], Memory[4], . . . , Memory[4294967292] |
MIPS assembly language
  Arithmetic
    add add $s1, $s2, $s3
    subtract sub $s1, $s2, $s3
    add immediate addi $s1, $s2, 5

## Slide 73
73
  Data transfer
    load word lw $s1, 100($s2)
    store word sw $s1, 100($s2)
    load byte lb $s1, 100($s2)
    store byte sb $s1, 100($s2)
    load upper immediate lui $s1, 100
  Conditional branch
    branch on equal beq $s1, $s2, 25
    branch on not equal bne $s1, $s2, 25
    set on less than slt $s1, $s2, $s3
    set on less than immediate slti $s1, $s2, 100
  Unconditional jump
    jump j 2500
    jump register jr $ra
    jump and link jal 2500

## Slide 74: 几点注意
74
原则：汇编程序可以不遵循编程原则
实例
1. 函数调用可以直接跳出，不通过bl 返回
同理，函数体中可以跳入，也可以从中直接跳出

## Slide 75
75
2. 形参超过4个怎么办？
  调用函数前，将第五个及以后的参数压堆栈
  函数内，弹出堆栈
  同理，返回值超过2个，也用堆栈
此规则亦可打破，用空闲的寄存器传递参数

## Slide 76
76
3. 函数调用中制定的寄存器规则，可以无视之
  a0-a3,v0-v1
    一般不拿来直接参与运算，为什么？
  s0-s7, t0-t9

## Slide 77: 2.9 Starting a Program
77
Start a C program in a file on disk to run
  Compiling
    C program  assembly language program
  Assembling
    Assembly language program  machine language module
    The object file for Unix systems typically contains six pieces:
    The object file header describes the size and position
    The text segment contains the machine language code
    The data segment
    The relocation information
    The symbol table
    The debugging information //release 版本与debugger版本

## Slide 78
78
  Linking
    Object modules(including library routine)  executable program
    6 pieces of the object file for Unix systems
    object file header, text segment, data segment,
    relocation information, symbol table, debugging information
    Place code and data modules symbolically in memory
    Determine the addresses of data and instruction labels
    Patch both the internal and external references
    文件头：通常可以用于记录该文件的类型
    问题：U盘上有且仅有一个65KB的winword文件，U盘被格式化,如何恢复?
      65KB为2扇区，读硬件扇区，利用文件头信息找到第一扇区，
      找到非零的扇区为第二扇区，如有多个，穷举也可

## Slide 79: 关于文件的一些背景知识
79
文件存在硬盘的逻辑分区中，具体存在扇区中，一般扇区为32KB
  因此，100个1字节的文件占据了100*32KB，100KB占据了4*32KB
文件
  起始扇区，存在目录中
  多个扇区的顺序，存在FAT表（文件分配表中）
  文件删除
    将目录中对应该文件的文件名首字节清空，设置fat表的各扇区为空闲
目录也是一个文件，每个文件在目录中是一条记录
内存碎片整理/磁盘碎片整理
  文件分配的原理：从0开始，找到一块整块的能存下，则放置文件；如果不够，分散分配
  内存：执行某程序，则从0开始，找到一块整块的能存下，则分配
  由于文件删除、内存释放造成碎片

## Slide 80
80
A translation hierarchy

## Slide 81: 静态链接库与动态链接库
81
库
  完成某个功能
  Printf：调用字符发生器，产生点阵，传输到显存上，显示
  静态链接库：直接链接
  动态链接库：可以作为外部调用，如扫描仪
静态链接库
  Windows: *.lib
  Linux : *.a
动态链接库
  Windows：*.dll
  Linux： *.so
类库
注意：编译器可以把库编入执行程序

## Slide 82
82
      Loading
        Determine size of text and data segments
        Create an large enough address space
        Copy instructions and data from executable file to memory
        Copy parameters (if any) to the main program onto the stack
        Initialize registers and set sp to the first free location
        Jump to a start-up routine

## Slide 83
83
Example 2.23 Linking object files
  Link the two object files in the next page
  Show updated addresses of the first few instructions of the executable file

## Slide 84
84
MIPS memory allocation for program and data

## Slide 85
85

## Slide 86
86
Address of X:
1000 8000 + FFFF 8000 = 1000 0000
Address of Y:
1000 8000 + FFFF 8020 = 1000 0020
微机的执行文件：
Com
Exe
PE

## Slide 87: 执行文件与进程
87
执行文件
  在硬盘上，非执行态
  如病毒样本
进程
  转载到内存
  可以细分为多个可以并发执行的线程
  如激活态病毒
  如何看线程: 任务管理器

## Slide 88: 计算机任何动作都是程序设计的
88
病毒
  组成：感染能力（自我复制），隐藏，破坏能力
  一个简单的
    感染：看到一个执行程序，就把病毒程序拷贝到执行程序最后，程序启动时加一条无条件跳转指令，跳到病毒处，病毒程序执行完成跳回首地址后
    隐藏：把执行程序拆封为n个，运行时组装为一体
    破坏：随便
程序都需要消耗内存
  System ideal也是程序，也消耗内存
  屏幕贴图也需要内存，如用一张10M图片做背景与黑色做背景，内存不一样，会影响哪些功能？

## Slide 89: EXE文件转移
89
把EXE的代码段中的一个字节写成00
在运行时，用计算结果(或其他来源)写入该位置
作用：防拷贝
参考：经典的针孔加密方法
  用针在磁盘上打孔，则该扇区的属性为坏块，以此为正版标记
  如果是磁盘拷贝的，则该块为CRC校验错误

## Slide 90: EXE文件加密
90
输入密码才能执行该文件？
普通的方法，先读密码，加密后判断是否继续
  问题：简单的修改执行文件即可破解
一般方法：
  第一段代码是密码验证
  若通过，则解密后续代码
    解密后长度=加密前，简单
    随便压缩
高级方法：
  分段加密，前一段的中间结果作为后续的解密用的密钥

## Slide 91: 一些关于器件编号的小贴士
91
1. 磁盘，0磁道在最外，磁头到0道速度
  快多少？非常明显
2. 主板上2个硬盘接口，IDE0，IDE1，分别有master，slave，能连接两个磁盘
  一个硬盘一个光驱，怎么连接？
    硬盘连IDE0 master，光盘连IDE1 master
  两个硬盘一个光驱，怎么连接
3. 两个内存，一个是四片组成，一个是一片组成，哪个好？片越少越好
  同理，硬盘有多个盘片，片越少越好。
4. 内存四个插槽，一根1G（速度100MHz），一根512M（速度133MHz），怎么插
  速度快的插0槽
  推论，操作系统在内存最低端，因此系统程序对内存的读写速度快
例外，通道无冲突或者访问非顺序的器件编号无效，如USB

## Slide 92: 2.10 An Example To Put it All Together
92
Three general steps for translating C procedures
  Allocate registers to program variables
  Produce code for the body of the procedures
  Preserve registers across the procedures invocation
Procedure swap
  C code
  swap ( int v[ ] , int k )
  {
  int temp ;
  temp = v[ k ] ;
  v[ k ] = v[ k + 1 ] ;
  v[ k + 1 ] = temp ;
  }

## Slide 93
93
  Register allocation for swap
  v ---- $a0 k ---- $a1 temp ---- $t0
  swap is a leaf procedure, nothing to preserve
  MIPS code for the procedure swap
    Procedure body
  swap: add $t1, $a1, $a1 # $t1 = k * 2
  add $t1, $t1, $t1 # $t1 = k * 4
  add $t1, $a0, $t1 # $t1 = v + ( k * 4 )
  # $t1 has the address of v[ k ]
  lw $t0, 0($t1) # $t0 ( temp ) = v[ k ]
  lw $t2, 4($t1) # $t2 = v[ k + 1 ]
  sw $t2, 0($t1) # v[ k ] = $t2
  sw $t0, 4($t1) # v[ k + 1 ] = $t0 ( temp )
    jr $ra # return to calling routine

## Slide 94
94
Procedure sort
  C code
  sort ( int v[ ] , int n )
  {
  int i , j ;
  for ( i = 0 ; i < n ; i = i + 1 ) {
  for ( j = i - 1 ; j >= 0 && v[j] > v[j+1] ; j = j - 1 )
  swap ( v , j ) ;
  }
  }
  Register allocation for sort
  v ---- $a0 n ---- $a1 i ---- $s0 j ---- $s1
  Passing parameters in sort
  Preserving registers in sort
  $ra , $s0, $s1, $s2, $s3

## Slide 95
95
  Code for the procedure sort
    Saving registers
  sort: addi $sp, $sp, -20 # make room on stack for 5 registers
  sw $ra, 16($sp) # save $ra on stack
  sw $s3, 12($sp) # save $s3 on stack
  sw $s2, 8($sp) # save $s2 on stack
  sw $s1, 4($sp) # save $s1 on stack
  sw $s0, 0($sp) # save $s0 on stack
    Procedure body
      Move parameters
    move $s2, $a0 # copy parameter $a0 into $s2 ( save $a0 )
    move $s3, $a1 # copy parameter $a1 into $s3 ( save $a1 )
      Outer loop
    move $s0, $zero # i = 0
    for1tst: slt $t0, $s0, $s3 # $t0 = 0 if $s0 >= $s3 (I>= n)
    beq $t0, $zero, exit1 # go to exit1 if $s0 >= $s3 (i >= n)

## Slide 96
96
      Inner loop
      addi $s1, $s0, -1 # j = i - 1
for2tst: slti $t0, $s1, 0 # $t0 = 1 if $s1 < 0 (j < 0)
    bne $t0, $zero, exit2 # go to exit2 if $s1 < 0 (j < 0)
    add $t1, $s1, $s1 # $t1 = j * 2
    add $t1, $t1, $t1 # $t1 = j * 4
    add $t2, $s2, $t1 # $t2 = v + (j * 4)
    lw $t3, 0($t2) # $t3 = v[j]
    lw $t4, 4($t2) # $t4 = v[j + 1]
    slt $t0, $t4, $t3 # $t0 = 0 if $t4 >= $t3
    beq $t0, $zero, exit2 # go to exit2 if $t4 >= $t3
      Pass parameters and call
    move $a0，$s2 # 1st parameter of swap is v ( old $a0 )
    move $a1，$s1 # 2st parameter of swap is j
    jal swap

## Slide 97
97
      Inner loop
    addi $s1, $s1, -1 # j = j - 1
    j for2tst # jump to test of inner loop
      Outer loop
    exit2: addi $s0, $s0, 1 # i = i + 1
    j for1tst # jump to test of outer loop
    Restoring registers
    exit1: lw $s0, 0($sp) # restore $s0 from stack
    lw $s1, 4($sp) # restore $s1 from stack
    lw $s2, 8($sp) # restore $s2 from stack
    lw $s3, 12($sp) # restore $s3 from stack
    lw $ra, 16($sp) # restore $ra from stack
    addi $sp, $sp, 20 # restore stack pointer
    Procedure return
    jr $ra # return to calling routine

## Slide 98: s0, t0
98
父函数保证：子函数能随便使用t0-9，返回给父函数的时候，t0-9可以随便改变
子函数保证：返回给父函数的时候，s0-7保持父函数调用子函数的值

## Slide 99
99
set: addi $sp,$sp,-52
sw $ra,48($sp)
move $s1, $a0
add $s0,$zero,$zero
loop: add $a1,$s0,$zero
slti $t0,$s0,10
beq $t0,$zero,Exit
jal lable1
sll $t1,$s0,4
add $t1,$t1,$sp
sw $v0,0($t1)
addi $s0,$s0,1
j loop
sw $s1, 4($sp)
sw $s0, 0($sp)
addi $v0, $sp, 44
Exit: lw $ra, 48($sp)
addi $sp,$sp,52
jr $ra
lable1: addi $sp,$sp,-4
sw $ra,0($sp)
jal lable2
slt $t0,$v0,$zero
beq $v0,$zero,Exit1
add $v0,$zero,$zero
lw $ra,0($sp)
addi $sp,$sp,4
jr $ra
Exit1: addi $v0,$zero,1
lw $ra,0(#sp)
addi $sp,$sp,4
jr $ra
lable2: sub $v0, $s1,$s0
jr $ra
很难翻译为C语言

## Slide 100: 问多少周期后程序运行结束，写出C语言
add $t1, $0, $0
addi $t2, $0, 10
Fun1: beq $t2, $t1, Exit1
addi $t1, $t1, 1
j Fun1
Exit1: addi $t2, $t2, -1
beq $t2, $t2, Exit2
jal Fun1
Exit2 jr $ra

## Slide 101: 问多少周期执行完成？并写出对应C语言。
Main： add $v0, $0, $0
addi $a0, $0, 10
Fun1: add $v0, $a0, $v0
subi $a0, $a0, -1
beq $a0, $0, Exit
jal Fun1
Exit: add $a0, $v0, $0
jal printf

## Slide 102: 已知fun函数输入为fun( int a[], i) 将a[i]与a[i+1]互换.写出对应的C语言
Main:
…
add $a0, $s0, $0 ; s0为main中数组int array[80], 内容为”abcdef”的起始地址
add $a1, $s1, $0 ; s1为main中的i
jal fun
sw a0, 0(t1)
sw a0, 0(t1)
add $a0, $s0, $0
add $a1, $s1, $0
jal swap
add $s0, $a0, $0
addi $s1, $a1, 4
add $a0, $s2, $0 ; s2为main中字符串“%s\n”的首地址

## Slide 103
add $a1, $s1, $0
jal printf
…
Fun: add t1, a1, a1
add t1, a1, a1
add t1, a0, t1
lw a0, 0(t1)
lw a1, 4(t1)
Swap: add $t1, $a0, $0
add $a1, $0, $a0
add $a0, $0, $t1
jr $ra

## Slide 104: 2.11 Arrays versus Pointers
Two C procedures
  Array version
  clear1 ( int array[ ], int size )
  {
  int i;
  for ( i = 0 ; i < size ; i = i + 1 )
  array[i] = 0;
  }
  Pointer version
    clear2 ( int *array, int size )
    {
    int *p;
    for ( p = &array[0] ; p < &array[size] ; p = p + 1 )
    *p = 0;
    }

## Slide 105
105
Assembly code for clear1 procedure (array version)
  move $t0, $zero # i = 0 ( $t0 = 0 )
  loop1: add $t1, $t0, $t0 # $t1 = i * 2
  add $t1, $t1, $t1 # $t1 = i * 4
  add $t2, $a0, $t1 # $t2 = address of array[ i ]
  sw $zero, 0($t2) # array[ i ] = 0
  addi $t0, $t0, 1 # i = i +1
  slt $t3, $t0, $a1 # $t3 = (i < size)
  bne $t3, $zero, loop1 # if ( i < size ) go to loop1
  This code works as long as size is greater than 0.

## Slide 106
106
Assembly code for clear2 procedure (pointer version)
  move $t0, $a0 # p = & array[ 0 ]
  add $t1, $a1, $a1 # $t1 = size * 2
  add $t1, $t1, $t1 # $t1 = size * 4
  add $t2, $a0, $t1 # $t2 = & array[ size ]
  loop2: sw $zero, 0($t0) # Memory[ p ] = 0
  addi $t0, $t0, 4 # p = p + 4
  slt $t3, $t0, $t2 # $t3 = (p < &array[size] )
  bne $t3, $zero, loop2 # if ( p < &array[size] ) go to loop2
  This code works as long as size is greater than 0.

## Slide 107
107
Compare the two versions:
Array version has the “multiply” and add inside loop
Pointer version reduces instructions/iteration from
7 to 4

## Slide 108: 2.12 PowerPC and 80x86 Instructions
108
The IBM/Motorola PowerPC
  Similarities with MIPS:
    All instructions are 32 bits long
    32 integer registers
    Data transfer is possible only with loads and stores
  Indexed addressing
    MIPS code
    add $t0, $a0, $s3 # $a0 has base of an array, $s3 is index
    lw $t1, 0($t0) # $t1 gets Memory[$a0 + $s3]
    Equivalent code in PowerPC
    lw $t1, $a0 + $s3 # $t1 gets Memory[$a0 + $s3]
  Update addressing
    MIPS code
    lw $t0, 4($s3) # $t0 = Memory[$s3 + 4]
    addi $s3, $s3, 4 # $s3 = $s3 + 4
    Equivalent code in PowerPC
    lwu $t0, 4($s3) # $t0 = Memory[$s3 + 4] ; $s3 = $s3 + 4

## Slide 109: Indexed and update addressing mode
109

## Slide 110
110
  Unique PowerPC instructions
    Load multiple and store multiple
    Instruction bc for loop
      C code
      for ( i = n ; i != 0 ; i = i - 1 ) { . . . }
      MIPS instructions
      Loop: . . .
      addi $t0, $t0, -1 # $t0 = $t0 - 1
      bne $t0, $zero, Loop # if $t0 != 0 go to Loop
      PowerPC instructions
      bc Loop, ctr != 0 # $ctr = $ctr - 1 ; if $ctr != 0 go to Loop
      Problems with the complex instructions above
    The instructions may not exactly match what the compiler needs
    A common case may be slower than a simple sequence

## Slide 111
111
The Intel 80x86
  Important milestones
    80x86 architecture in 1978
    8087 floating-point coprocessor in 1980
    80286 extended 8086 to 24 bits in 1982
    80386 extended 80286 to 32 bits in 1985
    Higher performance of 80486, Pentium, Pentium Pro in 1989-95
    Expand Pentium and Pentium Pro with MMX in 1997
  80x86 registers and data addressing modes
    80386 extended all 16-bit registers but segment ones to 32 bits
    GPR ( general-purpose register )
    Addressing modes
      Register indirect
      Based mode with 8- or 32-bit displacement
      Base plus scaled index
      Base plus scaled index with 8- or 32-bit displacement

## Slide 112: The 80386 register set
112

## Slide 113
113
80x86 integer operations
  Data movement instructions
  Arithmetic and logic instructions
  Control flow
  String instructions

## Slide 114: Some typical 80x86 instructions and their functions
114

## Slide 115: Typical 80x86 instruction format
115

## Slide 116: 2.13 History of Instruction Set Development
116
Accumulator Architectures
  Only 1 register for arithmetic instructions: accumulator
  Memory-based operand-addressing mode
Example 3.23 Compiling C code to accumulator instructions
  C code: A = B + C ;
  Accumulator instructions:
    load A adressB ; Acc = Memory[AddressB], or Acc = B
    add A adressC ; Acc = B + Memory[AddressC], or Acc = B + C
    store A adressA ; Memory[AddressA] = Acc, or A = B + C
Extended Accumulator Architectures

## Slide 117
117
General-Purpose Register Architectures
  Register-memory architecture (R—S TYPE)
    80386
    IBM 360
  Load-store or register-register architecture(R-R)
    CDC 6600
    MIPS
  DEC’s VAX architecture (Any combination TYPE)
    Allow any combination of registers and memory operands
    Memory-memory architecture
Example 3.24 Compiling C code to memory-memory instructions
  C code: A = B + C;
  Accumulator instructions:
    add AddressA, AddressB, AddressC

## Slide 118
118
Compact Code and Stack Architectures
  Variable-length instructions
    To match the varying operand specifications
    To minimize code size
  Stack model of execution
    All registers are abandoned
    Push, pop
Example 3.25 Compiling C code to stack instructions
  C code: A = B + C;
  Stack instructions:
    push adressC ; Top = Top+4; Stack[Top]=Memory[AddressC]
    push adressB ; Top = Top+4; Stack[Top]=Memory[AddressB]
    add ; Stack[Top-4]= Stack[Top]+Stack[Top-4];Top=Top-4;
    pop addressA ; Memory[AddressA]=Stack[Top]; Top=Top-4;

## Slide 119
119
High-Level-Language Computer Architecture
  Goal: hardware more like programming languages
  Finally failed
Reduced Instruction Set Computer Architecture (RISC )
  Fixed instruction lengths
  Load-store instruction sets
  Limited addressing modes
  Limited operations
  MIPS, Sun SPARC, Hewlett-Packard PA-RISC
  IBM PowerPC, DEC Alpha

## Slide 120: 2.14 Summary
120
Two principles of stored-program computers
  Use instructions as numbers
  Use alterable memory for programs
Four design principles
  Simplicity favors regularity
  Smaller is faster
  Good design demands good compromises
  Make the common case fast

## Slide 122
2.15