## Slide 1: Chapter 5 The processor : Datapath and control
Computer Organization & Design
The Hardware/Software Interface

## Slide 2: Computer Organization
计算机
CPU
Memory
I/O interface
Control unit
Datapath
Path: multiplexors
ALU
Registers
……

## Slide 3: Chapter Five The processor : Datapath and control
5.1 Introduction
5.2 Logic Design Conventions (skip)
5.3 Building a datapath
5.4 A Simple Implementation Scheme
5.5 A Multicycle Implementation
5.5 Microprogramming
5.6 Exception

## Slide 4: 5.1 The Processor: Datapath & Control
We’ll look at an implementation of the MIPS
Simplified to contain only (9 instructions) :
  memory-reference instructions: lw, sw
  arithmetic-logical instructions: add, sub, and, or, slt
  control flow instructions: beq, j
An Overview of the implementation
  For every instruction, the first two steps are identical
    Fetch the instruction from the memory
    Decode and read the registers
  Next steps depend on the instruction class
    Memory-reference Arithmetic-logical branches

## Slide 5: An abstract view of the implementation of MIPS(p288)

## Slide 6: Chapter Five The processor : Datapath and control
5.1 Introduction
5.2 Logic Design Conventions (skip)
5.3 Building a datapath
5.4 A Simple Implementation Scheme
5.5 A Multicycle Implementation
5.5 Microprogramming
5.6 Exception

## Slide 7: State Elements
Unclocked vs. Clocked
Clocks used in synchronous logic
  when should an element that contains state be updated?
cycle time
rising edge
falling edge

## Slide 8: Our Implementation
An edge triggered methodology
Typical execution:
  read contents of some state elements,
  send values through some combinational logic
  write results to one or more state elements

## Slide 9: D锁存器(D-Latch)
C
D
Q
Q
D
Q
C
Q
D锁存器的符号
C | D | Q(t + 1)
0 | X | hold
1 | 0 | Q=0：reset
1 | 1 | Q=1：set
C | D | S | R | Q(t + 1)
0 | X | X | X | hold
1 | 0 | 0 | 1 | Q=0：reset
1 | 1 | 1 | 0 | Q=1：reset
S
R
D锁存器功能表

## Slide 10: ALU
AND , OR
carryout
ADD

## Slide 11: ALU
AND, OR, ADD, SUB
AND, OR, ADD

## Slide 12: Chapter Five The processor : Datapath and control
5.1 Introduction
5.2 Logic Design Conventions (skip)
5.3 Building a datapath
5.4 A Simple Implementation Scheme
5.5 A Multicycle Implementation
5.5 Microprogramming
5.6 Exception

## Slide 13: The datapath there are ……
Name | Example | Comments
32 register | $s0-$s7,$t0-$t9, $zero,$a0-$a3, $v0-$v1 | Fast locations for data. In MIPS, data must be in registers to perform arithmetic. MIPS register $zero always equals 0. $gp(28) is the global pointer, $sp(29) is the stack pointer, $fp(30) is the frame pointer, and $ra(31) is the return address.
30 Word Addresses signals line | Memory[0], Memory[4] , …… , Menory[4294967292] | Accessed only by data transfer instructions. MIPS uses byte addresses, so sequential word addresses differ by 4. Memory holds data structures, arrays, and spilled registers, such as those saved on procedure calls.
Name | Register no. | Usage | Preserved on call
$zero | 0 | The constant value 0 | n,.a.
$v0-$v1 | 2-3 | Values for results and expression evaluation | no
$a0-$a3 | 4-7 | Arguments | no
$t0-$t7 | 8-15 | Temporaries | no
$s0-$s7 | 16-23 | Saved | yes
$t8-$t9 | 24-25 | More temporaries | no
$gp | 28 | Global pointer | yes
$sp | 29 | Stack pointer | yes
$fp | 30 | Framer pointer | yes
$ra | 31 | Return address | yes

## Slide 14: ALU OP for MIPS machine Language
Name | Format | Example |  |  |  |  |  | Comment
add | R | 0 | 18 | 19 | 17 | 0 | 32 | add $s1, $s2, $s3
sub | R | 0 | 18 | 19 | 17 | 0 | 34 | sub $s1, $s2, $s3
lw | I | 35 | 18 | 17 | 100 |  |  | lw $s1, 100($s2)
sw | I | 43 | 18 | 17 | 100 |  |  | sw $s1, 100($s2)
and | R | 0 | 18 | 19 | 17 | 0 | 36 | and $s1, $s2, $s3
or | R | 0 | 18 | 19 | 17 | 0 | 37 | or $s1, $s2, $s3
nor | R | 0 | 18 | 19 | 17 | 0 | 39 | nor $s1, $s2, $s3
addi | I | 12 | 18 | 17 | 100 |  |  | addi $s1, $s2,100
ori | I | 13 | 18 | 17 | 100 |  |  | ori $s1, $s2,100
beq | I | 4 | 17 | 18 | 25 |  |  | beq $s1, $s2,100
bne | I | 5 | 17 | 18 | 25 |  |  | bne $s1, $s2,100
slt | R | 0 | 18 | 19 | 17 | 0 | 42 | slt $s1, $s2,$s3
j | J | 2 | 2500 |  |  |  |  | j 10000(see section 2.9)
jr | R | 0 | 31 | 0 | 0 | 0 | 8 | j Sra
jal | J | 3 | 2500 |  |  |  |  | jar 10000(see section 2.9)
Field size |  | 6bits | 5bits | 5bits | 5bits | 5bits | 6bits | All MIPS instruction 32 bits
R-format | R | op | rs | rt | rd | shamt | funct | Arithmetic instruction format
i-format | I | op | rs | rt | address |  |  | Data transfer ,branch format

## Slide 15: Instruction execution in MIPS
Fetch :
  Take instructions from the instruction memory
  Modify PC to point the next instruction
Instruction decoding & Read Operand:
  Will be translated into machine control command
  Reading Register Operands, whether or not to use
Executive Control:
  Control the implementation of the corresponding ALU operation
Memory access:
  Write or Read data from memory
  Only LW/SW
Write results to register:
  If it is R-type instructions, ALU results are written to Rd
  If it is I-type instructions, Results are written to Rt

## Slide 16: Instruction fetching three elements
I
n
s
t
r
u
c
t
i
o
n
m
e
m
o
r
y
R
e
a
d
a
d
d
r
e
s
s
I
n
s
t
r
u
c
t
i
o
n
Add Sum
PC
Instruction memory
Program counter
Adder
The elements: instruction memory, program counter, adder
Instruction memory(only reads): combinational logic, no read control
Program counter: written at the end of every clock cycle, no write control

## Slide 17: Instruction fetching unit
P
C
I
n
s
t
r
u
c
t
i
o
n
m
e
m
o
r
y
R
e
a
d
a
d
d
r
e
s
s
I
n
s
t
r
u
c
t
i
o
n
4
A
d
d
CPU

## Slide 18: More Implementation Details
Abstract / Simplified View:

## Slide 19: Register File---- Built using D flip-flops
Read
5 bits
5 bits
5 bits
32 bits
32 bits
32 bits

## Slide 20: Register File
write
32 bits
rd or rt
5 bits
Write signals

## Slide 21
寄存器组 （register files）
  计算机基本部件（Datapath 的一部分）
  多个寄存器的集合
  寄存器地址、读/写控制

## Slide 22
8×32bits寄存器组硬件描述
module register_file(clk,cr,Address,Di,Do);
………… //端口及变量定义
initial begin
RegWrite<=0;
end
assign SEL=Address;
assign Y=~Yi;
assign clk1=clk&&Y[0];
assign clk2=clk&&Y[1];
assign clk3=clk&&Y[2];
assign clk4=clk&&Y[3];
assign clk5=clk&&Y[4];
assign clk6=clk&&Y[5];
assign clk7=clk&&Y[6];
assign clk8=clk&&Y[7];
register_32 rr0(clk1, Di, cr, Do0 );
register_32 rr1(clk2, Di, cr, Do1 );
register_32 rr2(clk3, Di, cr, Do2 );
register_32 rr3(clk4, Di, cr, Do3 );
register_32 rr4(clk5, Di, cr, Do4 );
register_32 rr5(clk6, Di, cr, Do5 );
register_32 rr6(clk7, Di, cr, Do6 );
register_32 rr7(clk8, Di, cr, Do7 );
decode_3_8 d(Address[2],Address[1],
Address[0],RegWrite,Yi);
MUX_8_1 mux(SEL,Do0,Do1,Do2,Do3,
Do4,Do5,Do6,Do7,Do);
endmodule
module register_32(cl,Di,cr,Dot);
………… //端口及变量定义
BUFG cck(cck,cl);
always@(posedge cl)
if (!cr)Dot<=0;
else Dot<=Di;
endmodule

## Slide 23: Implement the R type instruction
R-instruction format:
op(6)
rs(5)
rt(5)
rd(5)
Shamt(5)
func(6)
control
rs
rt
rd
b21-25
b16-20
b11-15
B negate | op | function
0 | 00 | and
0 | 01 | Or
0 | 10 | Add
1 | 10 | Sub
1 | 11 | Slt
Notes:   Shamt: Shift amount.
  Funct: Function.
  Op: Basic operation of the instruction opcode

## Slide 24: Implement the I type instruction
bit21-25
bit 16 -20
rs
rt
32bits data
bit0-15
lw $t0, 200($s2)
if $s2=1000，it will load a word in element number 1200 to $t0
op(6)
rs(5)
rt(5)
Immediate data

## Slide 25: Implementation of beq
0
1
to PC
op(6)
rs(5)
rt(5)
offset

## Slide 26: combine the implementation R-type and I type

## Slide 27: Chapter Five The processor : Datapath and control
5.1 Introduction
5.2 Logic Design Conventions (skip)
5.3 Building a datapath
5.4 A Simple Implementation Scheme
5.5 A Multicycle Implementation
5.5 Microprogramming
5.6 Exception

## Slide 28: Building the Datapath
Use multiplexors to stitch them together
Note : control signals
0
1
0
1
0
1

## Slide 29: Control
Analyse for cause and effect
Information comes from the 32 bits of the instruction
Selecting the operations to perform (ALU, read/write, etc.)
Controlling the flow of data (multiplexor inputs)
ALU's operation based on instruction type and function code

## Slide 30: Instruction Code
displacement
displacement
offset

## Slide 31: What should ALU do ?
e.g. what should the ALU do with these instructions
Example: lw $1, 100($2) OP rs rt 16 bit displacement
ALU control input
3 -types
Why is the code for subtract 110 and not 011?
(100011)35
2
1
100
B negate | op | function
0 | 00 | and
0 | 01 | Or
0 | 10 | Add
1 | 10 | Sub
1 | 11 | Slt
(101011)43
2
1
100
000000(00)
rs(5)
rt(5)
rd(5)
shamt
func(6)
lw
sw
R
00
00
10
ALU op

## Slide 32: Scheme of Controller
2-level decoder
First
Main
decoder
ALU
Decoder
Second
Signals for Other
Components
(7)
op(6)
rs(5)
rt(5)
rd(5)
shamt
func(6)
ALU operation(3)
ALU op(2)
instruction op code
(6)

## Slide 33: The ALU control is where and other signals(7)
1
0
0
1
0
1

## Slide 34: signals for datapath Defined 7+2 control
Signal name | Effect when deasserted(=0) | Effect when asserted(=1)
RegDst | Select register destination number from the rt(20:16) when WR | Select register destination number from the rd(15:11) when WB
RegWrite | None | Register destination input is written with the value on the Write data input
ALUScr | The second ALU operand comes from the second register file output (Read data 2) | The second ALU operand is the sign-extended lower 16 bits of the instruction.
PCSrc | The PC is replaced by the output of the addr that computes the value PC+4 | The PC is replaced by the output of the addr that computes the branch target.
MemRead | None | Data memory contents designated by the address input are put on the Read data output.
MemWrite | None | Data memory contents designated by the address input are replaced by value on the Write data input.
MemtoReg | The value fed to register Write data input comes from the Alu | The value fed to the register Write data input comes from the data memory.

## Slide 35: Designing the ALU decoder (Second level)
Must describe hardware to compute 3-bit ALU control input
Instruction opcode | ALUOp | Instruction operation | Funct field | Desired ALU action | ALU control Input
LW | 00 | Load word | xxxxxx | Load word | 0010
SW | 00 | Store word | xxxxxx | Store word | 0010
Beq | 01 | branch equal | xxxxxx | branch equal | 0110
R-type | 10 | add | 100000 | add | 0010
R-type | 10 | subtract | 100010 | subtract | 0110
R-type | 10 | AND | 100100 | AND | 0000
R-type | 10 | OR | 100101 | OR | 0001
R-type | 10 | Set on less than | 101010 | Set on less than | 0111

## Slide 36: Truth Table for ALU decoder
Describe it using a truth table (can turn into gates):
don’t care

## Slide 37: **The ALU control signals---- logic circuit
0 | x | x | 1
0 | 0 | x | x
x | x | x | x
x | x | x | 1
F1F0
F3F2
F1
1 | x | x | 1
0 | 0 | x | X
x | x | x | X
1 | x | x | 1
F1F0
F3F2
F2
0 | x | x | 0
0 | 1 | x | X
x | x | x | X
x | x | x | 1
F1F0
F3F2
F0
F3

## Slide 38: Designing the Main Control Unit (First level)
Main Control Unit function
  ALU op (2)
  Divided 7 control signals into 2 groups
    4 Mux
    3 R/W
ALU
control
Instruction op code (6)
ALU op (2)
Mux (4)
R/W (3)

## Slide 39
Truth Table for Main decoder

## Slide 40: Truth table

## Slide 41: Circuitry of main Controller
Simple combinational logic (truth tables)
opcode | output | 
000000 | R-format | 
100011 | lw | 
101011 | sw | 
000100 | beq | 
L/S 00
beq 01
R-type 10

## Slide 42: Our Simple Control Structure
All of the logic is combinational
We wait for everything to settle down, and the right thing to be done
  ALU might not produce right answer? right away
  we use write signals along with clock to determine when to write
Cycle time determined by length of the longest path
We are ignoring some details like setup and hold times
Instruction n
Instruction n+1

## Slide 43: The simple Datapath with the control unit
Read
address
Instruction
[31-0]
Instruction
memory
Read
register 1
Read
register 2
Write
register
Write
data
Read
data 1
Read
data 2
Registers
Address
Data
memory
Read
data
Write
data
0
M
U
X
1
0
M
U
X
1
1
M
U
X
0
0
M
U
X
1
ALU
ALU
result
Zero
Add
ALU
result
ALU
control
Control
Add
pc
4
Sign
extend
Instruction [31-26]
Instruction [25-21]
Instruction [20-16]
Instruction [15-11]
Instruction [15-0]
16
32
RegDst
Branch
MemRead
MemtoRead
ALUOp
MemWrite
ALUSrc
RegWrite
Instruction [5-0]
R-type |  |  |  |  | 
Op | rs | rt | rd | shamt | Funct
I-type |  |  | 
Op | rs | rt | Immediate
Jump-type | 
Op | address
Shift
left 2
Shift
left 2
26
Instruction [25-0]
1
M
U
X
0
jump
jump address[31-0]
28
PC+4[31-28]

## Slide 44: The Datapath in operation for R-type
Address
Data
memory
Read
data
Write
data
Add
ALU
result
Shift
left 2
Shift
left 2
26
Instruction [25-0]
jump address[31-0]
28
PC+4[31-28]
Sign
extend
Instruction [15-0]
16
32
I-type |  |  | 
Op | rs | rt | Immediate
Jump-type | 
Op | address
Read
address
Instruction
[31-0]
Instruction
memory
Read
register 1
Read
register 2
Write
register
Write
data
Read
data 1
Read
data 2
Registers
0
M
U
X
1
0
M
U
X
1
1
M
U
X
0
0
M
U
X
1
ALU
ALU
result
Zero
ALU
control
Control
Add
pc
4
Instruction [31-26]
Instruction [25-21]
Instruction [20-16]
Instruction [15-11]
RegDst
Branch
MemRead
MemtoRead
ALUOp
MemWrite
ALUSrc
RegWrite
Instruction [5-0]
R-type |  |  |  |  | 
Op | rs | rt | rd | shamt | Funct
1
M
U
X
0
jump
add sub and or slt

## Slide 45: The Datapath in operation for load
26
28
Instruction [15-11]
Write
data
Add
ALU
result
Shift
left 2
Read
register 2
Read
data 2
Instruction [20-16]
Instruction [5-0]
Shift
left 2
Instruction [25-0]
jump address[31-0]
PC+4[31-28]
R-type |  |  |  |  | 
Op | rs | rt | rd | shamt | Funct
Jump-type | 
Op | address
Read
address
Instruction
[31-0]
Instruction
memory
Read
register 1
Write
register
Write
data
Read
data 1
Registers
Address
Data
memory
Read
data
0
M
U
X
1
0
M
U
X
1
1
M
U
X
0
0
M
U
X
1
ALU
ALU
result
Zero
ALU
control
Control
Add
pc
4
Sign
extend
Instruction [31-26]
Instruction [25-21]
Instruction [15-0]
16
32
RegDst
Branch
MemRead
MemtoRead
ALUOp
MemWrite
ALUSrc
RegWrite
I-type |  |  | 
Op | rs | rt | Immediate
1
M
U
X
0
jump
load instruction

## Slide 46: The Datapath in operation for SW
Read
data
1
M
U
X
0
Write
register
Write
data
0
M
U
X
1
26
28
Instruction [15-11]
Add
ALU
result
Shift
left 2
Read
data 2
Instruction [5-0]
Shift
left 2
Instruction [25-0]
jump address[31-0]
PC+4[31-28]
R-type |  |  |  |  | 
Op | rs | rt | rd | shamt | Funct
Jump-type | 
Op | address
Read
address
Instruction
[31-0]
Read
register 1
Read
data 1
Registers
Data
memory
0
M
U
X
1
Control
Add
pc
4
Sign
extend
Instruction [31-26]
Instruction [25-21]
Instruction [15-0]
16
32
RegDst
Branch
MemRead
MemtoRead
ALUOp
MemWrite
ALUSrc
RegWrite
I-type |  |  | 
Op | rs | rt | Immediate
1
M
U
X
0
jump
store instruction
Read
register 2
Instruction [20-16]
Instruction
memory
Write
data
Address
0
M
U
X
1
ALU
ALU
result
Zero
ALU
control

## Slide 47: The Datapath in operation for BEQ
Write
data
Address
ALU
result
Read
data
1
M
U
X
0
Write
register
Write
data
0
M
U
X
1
26
28
Instruction [15-11]
Instruction [5-0]
Shift
left 2
Instruction [25-0]
jump address[31-0]
PC+4[31-28]
R-type |  |  |  |  | 
Op | rs | rt | rd | shamt | Funct
Jump-type | 
Op | address
Read
address
Instruction
[31-0]
Read
register 1
Read
data 1
Registers
Control
Add
pc
4
Sign
extend
Instruction [31-26]
Instruction [25-21]
Instruction [15-0]
16
32
RegDst
Branch
MemRead
MemtoRead
ALUOp
MemWrite
ALUSrc
RegWrite
I-type |  |  | 
Op | rs | rt | Immediate
1
M
U
X
0
jump
beq instruction
Read
register 2
Instruction [20-16]
Instruction
memory
0
M
U
X
1
ALU
ALU
control
Add
ALU
result
Shift
left 2
0
M
U
X
1
Data
memory
Read
data 2
Zero

## Slide 48: j instruction
instruction format
  j Label
Implementation
  pc = pc28~31 ## 26bits-address × 4
(000010)2
26 bits address

## Slide 49: The Datapath in operation for j
Registers
0
M
U
X
1
ALU
control
0
M
U
X
1
Read
data 2
Zero
Read
register 1
Read
data 1
Read
register 2
Add
ALU
result
Data
memory
Sign
extend
Instruction [25-21]
Instruction [15-0]
16
32
Instruction [20-16]
ALU
Shift
left 2
I-type |  |  | 
Op | rs | rt | Immediate
Write
data
Address
ALU
result
Read
data
0
M
U
X
1
Write
register
Write
data
0
M
U
X
1
Instruction [15-11]
Instruction [5-0]
R-type |  |  |  |  | 
Op | rs | rt | rd | shamt | Funct
Control
RegDst
Branch
MemRead
MemtoRead
ALUOp
MemWrite
ALUSrc
RegWrite
1
M
U
X
0
jump
jump instruction
Instruction
memory
Jump-type | 
Op | address
28
Shift
left 2
Instruction [25-0]
jump address[31-0]
PC+4[31-28]
Instruction [31-26]
26
Read
address
Instruction
[31-0]
Add
pc
4

## Slide 50: Single Cycle Implementation performance for lw
Calculate cycle time assuming negligible delays except:
  memory (2ns), ALU and adders (2ns), register file access (1ns)
2ns
2ns
2ns
1+1=ns

## Slide 51: **Performance in Single Cycle Implementation
Let’s see the following table:
Instruction class | Instruction memory | Register read | ALU | Data memory | Register write | Total
R-format | 2 | 1 | 2 |  | 1 | 6 ns
Load word | 2 | 1 | 2 | 2 | 1 | 8 ns
Store word | 2 | 1 | 2 | 2 |  | 7 ns
Branch | 2 | 1 | 2 |  |  | 5 ns
Jump | 2 |  |  |  |  | 2 ns
The conclusion:
  Different instructions needs different time.
  The clock cycle must meet the need of the slowest instruction. So, some time will be wasted.

## Slide 52: The CPU Performance Equation
CPU time=I CPI τ

## Slide 54
CPU performance is dependent upon three characteristics:
  clock cycle (or rate)
  clock cycles per instruction
  and instruction count.
It is difficult to change one parameter in complete isolation from others because the basic technologies involved in changing each characteristic are interdependent:
  Clock cycle time—Hardware technology and organization
  Clock cycle time—Hardware technology and organization
  Instruction count—Instruction set architecture and compiler technology

## Slide 55: MIPS (million instruction per second)
Three problems with MIPS:
  MIPS is dependent on the instruction set, making it difficult to compare MIPS of computers with different instruction sets.
  MIPS varies between programs on the same computer.
  Most importantly, MIPS can vary inversely to performance!
The bigger the MIPS, the faster the machine.

## Slide 56: Single Cycle Problems
:
  what if we had a more complicated instruction like floating point?
    If so,the waste of time will be more serious.
  wasteful of area. The reason is the following:
    Let’s see the instruction ‘mult’.This instruction needs to use the ALU repeatedly.But,in the single cycle implementation,one ALU can be used only once in one clock cycle.So,the instruction ‘mult’ will need many ALUs.The CPU will be very large.

## Slide 57: One Solution for Single Cycle Problems
One Solution:
  Use a smaller cycle time
  Let different instructions take different numbers of cycles
a Multicycle datapath:

## Slide 58: 期中考试 时间：夏学期第一周，随堂考 内容：截止单时钟（含）

## Slide 59: **Chapter Five The processor : Datapath and control
5.1 Introduction
5.2 Logic Design Conventions (skip)
5.3 Building a datapath
5.4 A Simple Implementation Scheme
5.5 A Multicycle Implementation
5.5 Microprogramming
5.6 Exception

## Slide 60: Multicycle Approach
We will be reusing functional units
  ALU used to compute address and to increment PC
  Memory used for instruction and data
We will use a finite state machine for control

## Slide 61
Notes: IR is used to generate controls during the following cycles

## Slide 62: Multicycle Approach
Break up the instructions into steps, each step takes a cycle
  balance the amount of work to be done
  restrict each cycle to use only one major functional unit
At the end of a cycle
  store values for use in later cycles
  introduce additional internal registers

## Slide 63: Analyse events: Five Execution Steps
IF：Instruction Fetch
ID：Instruction Decode and Register Fetch
EX（BC）：Execution, Memory Address Computation, or Branch Completion
MEM（WB）：Memory Access or R-type instruction completion
WB：Write-back step INSTRUCTIONS TAKE FROM 3 - 5 CYCLES!

## Slide 64: Multicycle Approach
a Multicycle datapath
shared unit
Notes: PC is a combinational unit which can be read or written at any time without control. The result from ALU is written to PC directly instead of through ALUOut.

## Slide 66
How does it control in Multicycle Approach

## Slide 67: Control signals
Signal name | Effect when deasserted(=0) | Effect when asserted(=1)
RegDst | Select register destination number from the rt(20:16) when WR. | Select register destination number from the rd(15:11) when WB.
RegWrite | None | Register destination input is written with the value on the Write data input
ALUScrA | The first ALU operand is the PC | The first ALU operand come from the A register.
MemRead | None | Memory contents at the location specified by the address input is put on the Memory data out.
MemWrite | None | Memory contents at the location specified by the address input are replaced by value on the Write data input.
MemtoReg | The value fed to register Write data input comes from the ALUOut | The value fed to the register Write data input comes from the MDA.
IorD | The PC is used to supply the address to the memory unit. | ALUOut is used to supply the address to the memory unit.
IRWrite | None | The output of memory is written into the IR.
PCWrite | None | The PC is written; the source is controlled by PCSource.
PCWriteCond | None | The PC is written if the zero output from the ALU is also active.

## Slide 68: Control signals
Signal name | Value | Effect
ALUOp | 00 | The ALU performs an add operation.
 | 01 | The ALU performs an subtract operation.
 | 10 | The funct field of the instruction determines the ALUoperation
ALUScrB | 00 | The second input to the ALU comes from the B register.
 | 01 | The second input to the ALU is the constant 4.
 | 10 | The second input to the ALU is the sign-extended, lower 16 bits of the IR.
 | 11 | The second input to the ALU is the sign-extended, lower 16 bits of the IR shift 2 bits.
PCSource | 00 | Output of the ALU(PC+4) is sent to the PC for writing.
 | 01 | The contents of ALUOut (the branch target address) are sent to the PC for writing.
 | 10 | The jump target address (IR[25:0]shifted left 2 bits and concatenated with PC+4[31:28]) is sent to the PC for writing.

## Slide 69
PC 的改变方式
  seq: pc = pc + 4
  beq： pc = pc + offset * 4
  j ： pc = pc31-28 + IR25-0 << 2

## Slide 70
  seq: pc = pc + 4
  beq：pc = pc + offset * 4
  j ：pc = pc31-28 + IR25-0 << 2

## Slide 71: Five Execution Steps
Instruction Fetch
Instruction Decode and Register Fetch
Execution, Memory Address Computation, or Branch Completion
Memory Access or R-type instruction completion
Write-back step INSTRUCTIONS TAKE FROM 3 - 5 CYCLES!

## Slide 72: Step 1: Instruction Fetch
Use PC to get instruction and put it in the Instruction Register.
  IR = Memory[PC];
Increment the PC by 4 and put the result back in the PC.
  PC = PC + 4;
Can be described simply using RTL "Register-Transfer Language" IR = Memory[PC]; PC = PC + 4;
Can we figure out the values of the control signals?
What is the advantage of updating the PC now?
Notes: MemRead, ALUSrcA=0, LorD=0, IRWrite,ALUSrcB=01, ALUop=00, PCSource=00, PCWrite

## Slide 73: **Step 2: Instruction Decode and Register Fetch
Read registers rs and rt in case we need them
Compute the branch address in case the instruction is a branch
RTL: A = Reg[IR[25-21]]; B = Reg[IR[20-16]]; ALUOut = PC + (sign-extend(IR[15-0]) << 2);
We haven’t set any control lines based on the instruction type (we are busy "decoding" it in our control logic)
Notes: ALUSrcA=0, ALUSrcB=11, ALUop = 00

## Slide 74: Step 3 (instruction dependent)
ALU is performing one of three functions, based on instruction type
Memory Reference ( lw / sw ): ALUOut = A + sign-extend(IR[15-0]);
R-type: ALUOut = A op B;
Branch: if (A==B) PC = ALUOut;
jump:
pc = pc31-28 + IR25-0 << 2
Notes: ALUSrcA=0, ALUSrcB=11, ALUop = 00

## Slide 75: Step 4 (R-type or memory-access)
Loads and stores access memory MDR = Memory[ALUOut]; # for lw
or Memory[ALUOut] = B; # for sw
R-type instructions finish Reg[rd]=Reg[ IR[15-11] ] = ALUOut; The write actually takes place at the end of the cycle on the edge

## Slide 76: Write-back step (step 5)
lw
  Reg[rt]=Reg[IR[20-16]]= MDR;
What about all the other instructions?

## Slide 77: Summary:

## Slide 78: Simple Questions
How many cycles will it take to execute this code? (21:5+5+3+4+4) lw $t2, 0($t3) lw $t3, 4($t3) beq $t2, $t3, Label #assume not add $t5, $t2, $t3 sw $t5, 8($t3) Label: ...
What is going on during the 8th cycle of execution? (p319)
  Answer: Calculating memory address
In what cycle does the actual addition of $t2 and $t3 take place?
  No.16

## Slide 79: Implementing the Control
Value of control signals is dependent upon:
  what instruction is being executed
  which step is being performed
Let’s go over the main control unit in the single-cycle implementation.

## Slide 80
Main control unit in the single-cycle implementation(p305,p313)
  R-type 0
  lw 35
  sw 43
  beq 4
Review

## Slide 81
Now let’s look at the ALU control unit. It does not need to be changed.
Review

## Slide 82
So,the following truth table remains the same.
As same as the single-cycle

## Slide 83
Do something different in each cycle
Two main ways to implement the control
  1. Finite state machine
  2. Microprogramming
Next, we will discuss the first method.
Difference in controller

## Slide 84
Notes: IR = Memory[PC];PC = PC + 4;
A = Reg[IR[25-21]];B = Reg[IR[20-16]];ALUOut = PC + (sign-extend(IR[15-0]) << 2);
ALUOut = A + sign-extend(IR[15-0]); ALUOut = A op B; if (A==B) PC = ALUOut; pc = pc31-28 + IR25-0 << 2
MDR = Memory[ALUOut]; Memory[ALUOut] = B; Reg[rd]=Reg[ IR[15-11] ] = ALUOut;
Reg[rt]=Reg[IR[20-16]]= MDR;

## Slide 85: Review: Finite state machines
Finite state machines:
  a set of states
  next state function (determined by current state and the input)
  output function (determined by current state and possibly input)

## Slide 86
Instruction execute flow
Instruction fetch/decode and register fetch
Memory access
instructions
R-type instructions
Branch instructions
Jump instructions
Start

## Slide 87
Instruction fetch / decode and Reg fetch(p76)
A
L
U
S
r
c
A
=
0
A
L
U
S
r
c
B
=
1
1
A
L
U
O
p
=
0
0
M
e
m
R
e
a
d
A
L
U
S
r
c
A
=
0
I
o
r
D
=
0
I
R
W
r
i
t
e
A
L
U
S
r
c
B
=
0
1
A
L
U
O
p
=
0
0
P
C
W
r
i
t
e
P
C
S
o
u
r
c
e
=
0
0
I
n
s
t
r
u
c
t
i
o
n
f
e
t
c
h
I
n
s
t
r
u
c
t
i
o
n
d
e
c
o
d
e
/
R
e
g
i
s
t
e
r
f
e
t
c
h
(
O
p
=
'
L
W
'
)
o
r
(
O
p
=
'
S
W
'
) ALUOp=00
(
O
p
=
R
-
t
y
p
e
)
(
O
p
=
'
B
E
Q
'
)
(
O
p
=
'
J
M
P
'
)
0
1
S
t
a
r
t
M
e
m
o
r
y
r
e
f
e
r
e
n
c
e
F
S
M
.
R
-
t
y
p
e
F
S
M
.
B
r
a
n
c
h
F
S
M
J
u
m
p
F
S
M

## Slide 88
M
e
m
W
r
i
t
e
I
o
r
D
=
1
M
e
m
R
e
a
d
I
o
r
D
=
1
A
L
U
S
r
c
A
=
1
A
L
U
S
r
c
B
=
1
0
A
L
U
O
p
=
0
0
R
e
g
W
r
i
t
e
M
e
m
t
o
R
e
g
=
1
R
e
g
D
s
t
=
0
M
e
m
o
r
y
a
d
d
r
e
s
s
c
o
m
p
u
t
a
t
i
o
n
(
O
p
=
'
L
W
'
)
o
r
(
O
p
=
'
S
W
'
)
M
e
m
o
r
y
a
c
c
e
s
s
W
r
i
t
e
-
b
a
c
k
s
t
e
p
(
O
p
=
'
S
W
'
)
(
O
p
=
'
L
W
'
)
4
2
5
3
F
r
o
m
s
t
a
t
e
1
T
o
s
t
a
t
e
0
M
e
m
o
r
y
a
c
c
e
s
s

## Slide 89
ALUSrcA=1
ALUSrcB=00
ALUOp=10
RegDst=1
RegWrite
MemtoReg=0
6
7
From state 1
To state 1
Op=R-type
Execution
R-type completion

## Slide 90
Branch
ALUSrcA=1
ALUSrcB=00
ALUOp=01
PCWriteCond
PCSource=01
8
From state 1
To state 1
Op=‘BEQ’
Branch completion

## Slide 91
J-type
PCSource=10
9
From state 1
To state 1
Op=‘J’
Jump completion

## Slide 92: Graphical Specification of FSM
R-type
jump
beq
lw
sw
Notes: DegDst = state7.(op=‘R-type’)

## Slide 93: The truth table for the 16 datapath control outputs, which depend only on the state inputs.(p84)

## Slide 94: The logic equations for the control unit shown in a shorthand form

## Slide 95: Implemented using a block of combinational logic and a register to hold the current state
Combinational
Control logic
State register
Input from instruction
Register opcode field
Datapath control output
Next state
Outputs
Inputs

## Slide 96: Chapter Five The processor : Datapath and control
5.1 Introduction
5.2 Logic Design Conventions (skip)
5.3 Building a datapath
5.4 A Simple Implementation Scheme
5.5 A Multicycle Implementation
5.5 Microprogramming
5.6 Exception

## Slide 97: Microinstruction format
Microinstruction
  control signal
  position of next Microinstruction
Representation
  split into some fields
  next position
    sequential
    dispatch table

## Slide 99: Microinstruction format(p76)
A=Reg[IR25-21], B=Reg[IR20-16]
(Reg fetch)

## Slide 100: Microinstruction format
Mem address is from

## Slide 101
Two dispatches

## Slide 102: Steps of Instructions

## Slide 103: Microprogramming
A specification methodology
  appropriate if hundreds of opcodes, modes, cycles, etc.
  signals specified symbolically using microinstructions
address
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001

## Slide 104
Two dispatches

## Slide 105: 微指令编码
ALU | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | ALUOp1
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | ALUOp0
SRC1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | ALUSrcA
SRC2 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | ALUSrcB1
 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | ALUSrcB0
Register control | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | IRWrite
 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | RegWrite
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | RegDst
 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | MemtoReg
Memory control | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | MemRead
 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | MemRead
 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | IorD
PCWite | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | PCSource1
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | PCSource0
 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | PCWrite
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | PCWriteCond
Seq | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | Addrctl1
 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | Addrctl0
Label
ALU
control
SRC1
SRC2
Register
control
Memory
PCWrite
control
Sequencing
Fetch
Add
PC
4
Read PC
ALU
Seq
Add
PC
Extshft
Read
Dispatch 1
Mem1
Add
A
Extend
Dispatch 2
LW2
Read ALU
Seq
Write MDR
Fetch
SW2
Write ALU
Fetch
Rformat1
Func code
A
B
Seq
Write ALU
Fetch
BEQ1
Subt
A
B
ALUOut-cond
Fetch
JUMP1
Jump address
Fetch
Ten states

## Slide 106: Microprogramming
What are the Microinstructions?

## Slide 107
Details
见光盘

## Slide 108
ALU | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | ALUOp1
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | ALUOp0
SRC1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | ALUSrcA
SRC2 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | ALUSrcB1
 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | ALUSrcB0
Register control | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | IRWrite
 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | RegWrite
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | RegDst
 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | MemtoReg
Memory control | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | MemRead
 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | MemRead
 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | IorD
PCWite | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | PCSource1
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | PCSource0
 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | PCWrite
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | PCWriteCond
Seq | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | Addrctl1
 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | Addrctl0
S
T
A
T
E
3
2
1
0
0011
0101
0110
1001
1001
0010
0
Opcode
Lw
sw
R
J
Beq
Lw
sw
1

## Slide 109: Chapter Five The processor : Datapath and control
5.1 Introduction
5.2 Logic Design Conventions (skip)
5.3 Building a datapath
5.4 A Simple Implementation Scheme
5.5 A Multicycle Implementation
5.5 Microprogramming
5.6 Exception

## Slide 110: 5.6 Exception
The cause of changing CPU’s work flow :
  Control instructions in program (bne/beq, j, jal , etc)
  It is foreseeable in programming flow
  Something happens suddenly (Exception and Interruption)
  It is unpredictable
Unexpected events
  Exception: from inside processor ( overflow, undefined instruction, etc)
  Interruption : from outside processor ( input /output )

## Slide 111: 5.6 Exception
Exception
  An Exception is a unexpected event from inside processor.
We follow the MIPS convention, using the term exception to refer to any unexpected change in control flow.
Here we will discuss two types of exceptions :
  arithmetic overflow
  undefined instruction

## Slide 112: How Exceptions Are Handled
When exception happens, the processor must do something.
The predefined process routines are saved in memory when computer starts.
Problem: how can CPU goto relative routine when an exception occurs.
CPU should know
  the cause of exception
  which instruction generates the exception

## Slide 113: How Exceptions Are Handled
Design
  add a register: exception program counter(EPC)
  save the address of the offending instruction
  add a status register: cause register( CauseReg)
  hold a field that indicates the reason for the exception.
  0 undefined instruction
  1 overflow
  Another method is to use vector interrupts
bit0 =
vector address
Exception type
c0 00 00 00 H
c0 00 00 20H
undefined instr
overflow

## Slide 114: How Control Checks for Exceptions
add control signal
  CauseWrite for CauseReg
  EPCWrite for EPC
  EPC = PC - 4 (completed by ALU)
process of control
  CauseReg = 0 or 1
  EPC = PC - 4
  PC <--- address of process routine ( ex. c0000000 )

## Slide 115
How Control Checks for Exceptions

## Slide 116: How Control Checks for Exceptions
detect exceptions
  Undefined instruction
  When no next state is defined from state 1 for op value. New state 10 is introduced.
  Overflow
  Overflow occurred only in R-type instruction. Overflow is provided as an output from the ALU. This signal is used in the modified FSM to specify an additional state 11 for state 7 .